## Slide 1: Assistance for people with Disabilities
ΟΜΑΔΑ 8
ΚΩΤΣΟΠΟΥΛΟΣ ΙΩΑΝΝΗΣ
ΚΑΡΒΟΥΝΗΣ ΠΑΣΧΑΛΗΣ
Architecture & Alpha version

## Slide 2: Critical Sensors
Camera
Heart Rate Sensor
Gyroscope and Accelerometer
Phone Sensors:
      Microphone
      GPS

## Slide 3: Possible Use Cases
Real-Time Assistance & Navigation from VLM/LLM
Health Monitoring & Early Risk Detection
Emergency SOS & Automatic Alerts in case of emergency
Caregiver Portal-Live communication and intervention

## Slide 4
Glasses-Client
RT DEPENDENT
Local VLM/LLM
Minimal health watchdog
Glasses Controller
MQTT Broker
ContextBroker
Grafana
VMS
Ingestion point
VLM/LLM
Backend
Front
MQTT
MQTT
MQTT
MQTT
MQTT
HTTP
HTTP
HTTPS
HTTPS
WebRTC
NGSI
MQTT
Sensor Streams
Sensor Streams
Sensor Streams
Sensor Streams
Sensor Streams
Video Stream
Frames
Notifications
Notifications
Caretaker Messages/AI answers
Caretaker
Messages/AI
answers
GPS/Text from speech
Sensor Streams
Sensor Streams
Users’ Info
AI Queries
WebRTC
Video Stream
MQTT Broker
Wi-Fi
GPS
VOICE REC
VIDEO STREAMING
MCP Server
HTTP
Notifications
Node.js
HTTP
AI GATEWAY/PROXY
VIDEO INGESTION
TTS
APP
SQlite
InfluxDB
Front
Glasses
Sensor Streams

## Slide 5
GLASSES CONTROLLER
Glasses-Client
  Collects sensors’ outputs
  Communicates with Cloud MQTT-Broker
  Sends messages to HUD
Local VLM/LLM
  Tiny on device models
  Used only in offline mode
RT Dependent
  Real-time processing of high-frequency sensor data (gyroscope)
Minimal Health Watchdog
  Fall Detection
  Cardiac Monitoring
  Emergency Triggers
VIDEO Streaming
  Captures camera frames
  Sends frames to VMS

## Slide 6
USER’S PHONE APP &
CLOUD ENTRY MQTT BROKER & VMS
Phone App
  Publishes GPS data stream to cloud broker
  Records voice queries, uses voice to text and publishes text to Cloud broker
  Receives AI outputs and uses Text-to-Speech (TTS) to respond audibly
MQTT Broker
  Is the central point of communication linking the Edge, the App and the Cloud
  Routes the data
  Critical for scalability and real time responsiveness
VMS
  Receives video from video streaming and routes frames to frontend or backend

## Slide 7
INGESTION & CONTEXT MANAGEMENT
Ingestion Point
  Normalizes/Validates data
  Forwards data either to InfluxDB for storing or to context broker
Context Broker
  Real-Time State Management
  Event Subscriptions & Notifications
  Standardized API (NGSI/NGSI-LD)
MQTT Broker
  Publishes notifications backend and frontend

## Slide 8
Backend
  Processes sensor stream
  Connects AI Agents with Cloud via the AI gateway
  Forwards frames from VMS to AI gateway via the Video Ingestion point
  Includes Care Giver portal backend (Node.js) which receives data from influxDB and notifications
  Publishes the AI answers and Care Giver messages to Cloud entry MQTT broker
  Stores user’s info in SQlite database
Frontend-Care Giver Portal
  Displays graphs received from Grafana
  It supports live streaming from glasses camera and live communication through messages
  It receives critical notifications send from Cloud
AI Agents
  LLM
    Acts as logical router deciding to either answer the query itself or send it to VLM
  VLM
    Answers the queries using frames captured by VMS and communicates with *MCP server, which contains CV, for support to analyze the frames
BACKEND-FRONTEND & AI AGENTS

## Slide 9: LIVE VIEW PAGE
Access to the glasses’ camera by the caregiver for live monitoring.

## Slide 10: LOCATION TRACKING PAGE
Tracking the user’s location via phone app

## Slide 11: USER’S HEALTH MONITORING
Heart rate
User’s speed
Pedometer

## Slide 12: NOTIFICATIONS PAGE
Device status
Important alert for possible emergency

## Slide 13: COMMUNICATION PAGE
Messages among user and care giver

## Slide 14: PHONE APP & APP INVENTOR BLOCKS

## Slide 15: PROJECT TIMELINE
Glasses Controller
Local VLM/LLM integration (planned)
RT Dependent integration (planned)
Minimal Health Watchdog integration (planned)
Cloud
Phone app (almost completed)
Brokers communication logic (under development)
Video streaming logic (later work)
Databases (influxDB & SQlite) (under development)
Backend & Frontend
AI gateway (Completed)
Video Ingestion (later work)
BFF & Frontend (planned)

## Slide 16
THANK YOU FOR YOUR ATTENTION